## Slide 1: Course 227 Lab 6 – Waveguide Structures CST Microwave Studio
Dr Harry Marks
h.marks@lancaster.ac.uk

## Slide 2: Objectives:
Become more familiar with CST Microwave Studio by simulating new structures:
  Be able to identify different modes at the input port.
  Finding the cut-off frequency using CST and via calculation.
  Calculate Impedance.

## Slide 3
Set up a waveguide with inner dimensions a = 4mm, b = 2mm. Set the frequency range as 95-105 GHz. This can be done by clicking on the tab shown below:

## Slide 4: By clicking on port1 from the left hand menu a pop-up appears. Here you can select the number of modes which can be excited at this port.

## Slide 5: Reminder: Click on Setup Solver to run the simulation. You can choose which port mode you want to excite. Then click start.

## Slide 6: TE10

## Slide 7: TE20

## Slide 8: TE01

## Slide 9: Note the details in the purple square in slides 6 and 7.
Each mode has a different wave impedance ().
Each mode has a different cut-off frequency.
Make a note of the cut-off frequencies and impedances of the first three TE modes.
Using the lecture 16 notes compare these values with values you calculate for the cut-off and impedance for these three modes. Include as I have done above a screenshot of the first three modes as well as your calculation for comparison.

## Slide 10: Calculating the wave impedance, that is ,
For a mode to propagate we require to be real, so: